## Slide 1: Co-Simulation between detailed building energy performance simulation and Modelica HVAC component models
Andreas Nicolai and Anne Paepcke
andreas.nicolai@tu-dresden.de

## Slide 2: Starting point: NANDRAD - Building energy simulation engine
Multi-zone building model
Realistic building physics (spatially resolved walls/storage members)
CVODE time integration engine (error controlled variable-order, variable step method)
Algebraic relations embedded in ODE equations
Using Newton-Krylov-method for non-linear system of equations
Special problem-specific sparse matrix structures and preconditioners

## Slide 3: Multi-zone model, embedded equipment loop and sparsity pattern
Jacobian Matrix Sparsity Pattern
Instead of hard-coded equipment models rather use Modelica-based equipment models

## Slide 4: Idea tested: get everything into Modelica via Code-generator
A lot of code like this!
Symbolic analysis (OpenModelica/ SimulationX)
really slow on large
Models

## Slide 5: Idea tested: get everything into Modelica via Code-generator
A lot of code like this!
Symbolic analysis (OpenModelica/ SimulationX)
really slow on large
Models
Alternative:
Export building as Functional Mockup Unit (FMU) and connect to Modelica equipment model

## Slide 6: Software architecture of NANDRAD engine
Integrator Implementation
Physical Model Implementation
setTime(t)
init(model)
step()
t()
solves ODE system of type ydot = f(t,y)
implicit solver with Newton-Raphson iteration
Solver Control System
Implements core integration loop: calls step() function in Integrator, also manages output schedules
control functions
query functions
y0()
t0()
tEnd()
implements physical model equations and the computation of the system function f(t,y)
state of object changes only through calls of
control functions
n()
setY(y)
ydot()
yOut(t_out)
stepCompleted(t,y)
writeOutputs(...)

## Slide 7: Export ODE system function via FMU for ModelExchange
Integrator Implementation
Physical Model Implementation
setTime(t)
init(model)
step()
t()
solves ODE system of type ydot = f(t,y)
implicit solver with Newton-Raphson iteration
Solver Control System
Implements core integration loop: calls step() function in Integrator, also manages output schedules
control functions
query functions
y0()
t0()
tEnd()
implements physical model equations and the computation of the system function f(t,y)
state of object changes only through calls of
control functions
n()
setY(y)
ydot()
yOut(t_out)
stepCompleted(t,y)
writeOutputs(...)
Corresponds to FMI ModelInterface

## Slide 8: Export physical model and integrator as FMI for Co-Simulation
Integrator Implementation
Physical Model Implementation
setTime(t)
init(model)
step()
t()
solves ODE system of type ydot = f(t,y)
implicit solver with Newton-Raphson iteration
Solver Control System
Implements core integration loop: calls step() function in Integrator, also manages output schedules
control functions
query functions
y0()
t0()
tEnd()
implements physical model equations and the computation of the system function f(t,y)
state of object changes only through calls of
control functions
n()
setY(y)
ydot()
yOut(t_out)
stepCompleted(t,y)
writeOutputs(...)
To be replaced by Co-Simulation Master
Corresponds to FMI Co-Simulation interface

## Slide 9: FMU Generation Process
Starting with BIM  Project file for standalone building simulation
Indicate which thermal zones shall be heated/cooled and be used in the FMU-interface
Run design day simulations (heating/cooling)
Generate report file (zone ID – variable index mapping, design loads)
Create ModelDescription.xml
Create Modelica-Wrapper and Adapter models (corresponding to project)
Compress project file, all database files, pre-compiled FMU-DLL and additional dependent libraries into FMU-archive
Steps 3 to 7 are done automatically by NANDRAD solver via command line:
NandradSolver RowHouse_var1.nandrad --fmu-export=RowHouse_var1.fmu
(exported FMU is exported as FMI version 2, for both ME and CS)

## Slide 10: FMI Interface to NANDRAD Building Model FMU

## Slide 11: FMI Interface to NANDRAD Building Model FMU
Outputs
Climate data

## Slide 12: FMI Interface to NANDRAD Building Model FMU
Outputs
Climate data
Zone air/ radiant temperatures

## Slide 13: FMI Interface to NANDRAD Building Model FMU
Outputs
Climate data
Zone air/ radiant temperatures
Setpoint temperatures (schedules)

## Slide 14: FMI Interface to NANDRAD Building Model FMU
Outputs
Climate data
Zone air/ radiant temperatures
Setpoint temperatures
Electric loads
Warm water consumption

## Slide 15: FMI Interface to NANDRAD Building Model FMU
Outputs
Climate data
Zone air/ radiant temperatures
Setpoint temperatures
Electric loads
Inputs
Convective and radiant thermal loads

## Slide 16: FMI Interface to NANDRAD Building Model FMU
Outputs
Climate data
Zone air/ radiant temperatures
Setpoint temperatures
Electric loads
Inputs
Convective and radiant thermal loads
Zone specific inputs/outputs scale with number of zones! Manual connection ???

## Slide 17: Application Scenario 1: Import into Modelica environment
Building FMU
Demonstration Case 1

## Slide 18: Application Scenario 1: Import into Modelica environment
Building FMU
Demonstration Case 2

## Slide 19: Introduce Modelica-Adapter Models (autogenerated)

## Slide 20: Introduce Modelica-Adapter Models (autogenerated)
Connectors match exactly native FMU connectors by name
Connectors match complex ports of HVAC library

## Slide 21: Introduce Modelica-Wrapper Models (autogenerated)
Imported FMU
Adapter model

## Slide 22: Introduce Modelica-Wrapper Models (autogenerated)
The building model from point of view of the user within the Modelica environment

## Slide 23: Introduce Modelica-Wrapper Models (autogenerated)
Only need to connect a few ports

## Slide 24
Export FMU – with only adapter variables
as FMI interface variables
Application Scenario 2: Export equipment FMU

## Slide 25
Application Scenario 2: Co-Simulation with CoSim-Master
Open-Source Co-Simulation Master developed at TU Dresden, Germany
http://mastersim.sourceforge.net

## Slide 26
Co-Simulation: fixed-step size – stability problems

## Slide 27
Co-Simulation: Fixed step size – Gauss-Seidel better

## Slide 28
Co-Simulation: with adaptive step-size (error controlled)

## Slide 29
Summary
Building energy simulation NANDRAD can now be used as FMI for ME/CS (version 2, with get/set state capability)
Use case 1 (within Modelica environment):
  NANDRAD-FMU substitutes simpler building models (when needed)
  Modelica-Wrapper-Models significantly simplifies connecting FMUs with hundreds of input/output variables
Use case 2 (Equipment FMU + Building FMU running in external Co-Simulation Master)
  Use of adapter models simplifies setup of co-simulation szenario
  Choice of master algorithm has great impact on stability/accuracy and performance

## Slide 30: Co-Simulation between detailed building energy performance simulation and Modelica HVAC component models
Andreas Nicolai and Anne Paepcke
andreas.nicolai@tu-dresden.de

## Slide 31: Internal functionality (only for discussion)

## Slide 32: Functionality within Co-Simulation Master
Model acts as a Co-Simulation slave
Interacts with Master through get/set functions
Time integration is done within a communication step when Master calls doStep()

## Slide 33
t_commStart
Integration time frame
t0
y
Master->doStep(...)
t_commEnd
Master requests slave to integrate over a communication interval starting from a known solution

## Slide 34
t_commStart
Integration time frame
Time steps
dt
t0
y
Master->doStep(...)
t_commEnd
Integrate step-by-step and adapt time step size based on local error control
computed solutions after
completed integration step

## Slide 35
t_commStart
Integration time frame
Time steps
dt
t0
y
Master->doStep(...)
t_commEnd
Integrate until communication interval has been completed
computed solutions after
completed integration step

## Slide 36
t_commStart
Integration time frame
Time steps
dt
t0
y
Master->doStep(...)
t_commEnd
Limit time step to match interval end
Limit last time step to hit communication interval end time exactly
computed solutions after
completed integration step

## Slide 37
t_commStart
Integration time frame
Time steps
dt
t0
y
Master->doStep(...)
t_commEnd
Outputs may be requested at different times than time step or communication interval end time
Outputs
output_dt
computed solutions after
completed integration step
Limit time step to match interval end

## Slide 38
t_commStart
Integration time frame
Time steps
dt
t0
y
Master->doStep(...)
t_commEnd
Outputs are interpolated in last completed integration step (can be several outputs)
Outputs
output_dt
computed solutions after
completed integration step
Limit time step to match interval end
interpolated solution at output time point

## Slide 39: Things to consider…
Limit last time step
When interpolating model state backwards in last step, restore model state to end of communication interval before returning control to master
… otherwise pretty straight forward …

## Slide 40: Iterative Master algorithms
Gauss-Jacobi, Gauss-Seidel, Newton
Master requests Slave to store its state
Master can request Slave to store multiple states
Master requests Slave to reset its state back to a previously stored state (roll-back)
Related functions:
  fmi2Serialize(), fmi2Deserialize(), fmi2SerializedFMUstateSize(), fmi2GetFMUState(), fmi2SetFMUState()

## Slide 41: Getting and Setting FMU State
State is defined by:
  Integrator (conservation variables of ODEs)
  LES solver (for direct solvers factorized Jacobian)
  Jacobian matrix (unfactorized)
  Preconditioner (unfactorized and in case of ILU also factorized)
  Model state (e.g. hysteresis variables)

## Slide 42: Getting and Setting FMU State
Fragmented memory structures
Direct copy not meaningful (and not fast)
 Copy into sequential memory first
Implement first serialize and deserialize functionality

## Slide 43: Getting FMU State via Serialization Typical implementation of fmi2GetFMUState():

## Slide 44: Serialization into sequential memory
Fragmented memory structures
Sequential memory
"Append"-pointer

## Slide 45: Serialization into Sequential Memory
Fragmented memory structures
Sequential memory
"Append"-pointer

## Slide 46: Serialization into Sequential Memory
Fragmented memory structures
Sequential memory
"Append"-pointer

## Slide 47: Serialization into Sequential Memory
Fragmented memory structures
Sequential memory
"Append"-pointer

## Slide 48: Serialization into Sequential Memory
Fragmented memory structures
Sequential memory
"Append"-pointer

## Slide 49: Serialization into Sequential Memory
Maintainable code  Single code for:
Size calculation
Copy into sequential memory
Copy back from sequential memory
For C compatibility (e.g. for CVODE integrator) use Macros

## Slide 50: Serialization into Sequential Memory

## Slide 51: Serialization into Sequential Memory

## Slide 52: Serialization into Sequential Memory
Single code for mapping memory depending on selected operation type (op):

## Slide 53: Aspects of creating a coupled building energy simulation
Adding FMI ME+CS interface to a stand-alone simulation engine
Implementing FMU v2 setting/getting-state capability
FMU generation process + resource handling
Application scenarios
Interface conventions
Usability (Modelica-Wrapper/Adaptors)
Demonstration cases (findings and experience gained)